## Slide 1
NAME :- ROHAN RAVI
ROLL NUMBER :- 16800117033
STREAM :- CSE

## Slide 2: Link state routing

## Slide 3: *Outline
Overview
Features of Link-State routing
link-state routing algorithm
OSPF
IS-IS
Advantages and Disadvantages of LS routing protocols

## Slide 4: Overview
One of two main classes of interior gateway routing protocols OSPF, IS-IS
Performed by every switching node in the network

## Slide 5: Basic Concept
every node creates a map of the connectivity to the network
This graph shows which nodes are connected to which other nodes
Each node calculates the next best logical path to the destination
Collection of best paths form the routing table of the node

## Slide 6: Features of Link-state routing
Link-state advertisement (LSA) or Link-state Packet(LSP)
a small packet of routing information that is sent between
routers
Topological database or Link-state Database
a collection of information gathered from LSAs

## Slide 7
SPF algorithm
a calculation performed on the database that results in the
SPF tree
Routing table
a list of the known paths and interfaces

## Slide 8: link-state routing algorithm
1. Each router is responsible for meeting its neighbours and
learning their names.
Used a Hello Protocol, which send a data packet contains RID
and address of the network on which the packet is being sent
2. Each router constructs a LSP/LSA which consists of a list of
names and cost for each of its neighbours.

## Slide 9
3. The LSP/LSA is transmitted to all other routers. Each router
stores the most recently generated LSP/LSA from each
other router.
Link-state flooding: Sequencing and Aging procedures
Each routers store the identical Link State Database

## Slide 10
4. Each router uses complete information on the network
topology to compute the shortest path route to each
destination node.
Use SPF or Dijkstra’s algorithm to calculate the shortest path

## Slide 11: Open Shortest Path First (OSPF)
A routing protocol developed for Internet Protocol networks by the Interior Gateway Protocol (IGP)
Based on the Dijkstra’s Algorithm
Serving large, heterogeneous internetworks
Equal-cost
Multipath routing
Routing based on upper-layer type-of-service (TOS) requests

## Slide 12: IS-IS
Intermediate System-to-Intermediate System (IS-IS)
That floods the network with link-state information to build a complete, consistent picture of network topology
Each IS-IS router independently builds a database of the network's topology
IS-IS uses Dijkstra's algorithm for computing the best path through the network

## Slide 13: Advantages and Disadvantages of LINK STATE routing
Advantages
Smaller routing tables
Only a single optimal route for each network ID is stored in the routing table.
Low network overhead
do not exchange any routing information when the internetwork has converged.

## Slide 14
Ability to scale.
scale well to large and very large internetworks.
Lower convergence time.
have a much lower convergence time and the internetwork is converged without routing loops.

## Slide 15
Disadvantages
Complex
much more complex and difficult to understand than DV routing protocols.
More difficult to configure.
implementation requires additional planning and configuration.

## Slide 16
Resource intensive.
For very large internetworks, the LS database and the calculation of routing table entries can be memory and processor intensive.

## Slide 17: THE END